## Slide 1: There and Back Again - The Practicality of GPU Accelerated Digital Audio
Harri Renney & Benedict R. Gaster
Computer Science Research Centre
Tom Mitchell
Computer Science and Creative Technologies
Notes: Introduce self.
PhD second year with Tom & Ben

## Slide 2: Latency
0.14ms
Notes: The time interval between stimulation and response.
From time you send a message, until you receive a message.
The time a buffer of samples is requested until the time it is received.
Often a concern people are made aware in networks and “internet speeds”. Where it is the average time from a request to the packet of data arriving.

## Slide 3: Jitter
0.08ms
Therefore, jitter = 0.06ms
0.14ms
Notes: The difference in time between two consecutive events.

## Slide 4: Round-trip Audio Latency
ADC
DAC
OS & Driver
OS & Driver
Audio Code
GPU
[1]
Notes: Andrew McPherson great job covering this in his Bela talk:
Let’s establish how latency builds up. In this typical real-time format, there are many sources of latency.
Many of these are out of control, intrinsically involve latency.
We have control of audio code and what happens there.
Adding another source of latency from the GPU. Is it worth it? Can it possibly fit into the real-time constraints still.

## Slide 5: Buffering
.
Notes: The agreed upon buffer time is a crucial factor in real-time environments.
Smaller buffer size = Decreased latency and jitter. Increased overall execution time. (Therefore harder to meet sample rate)
Larger buffer size = Increased latency and jitter. Decreased overall execution time.

## Slide 6: General-Purpose GPU Compute
Notes: Explain what a GPU is.
Explain what GPGPU is.
A massively parallel programing architecture.
Promotes heterogenous computing.
@ToDo – Show some other things that could be running on the GPU.

## Slide 7: Real-Time Benchmarks

## Slide 8: Real-time Requirements
[2] [3]
Notes: Ideal and minimum requirements for operating with audio in real-time.
We have chosen these requirements based off studies referenced in the paper ([1][2])

## Slide 9: Baseline Bidirectional Test
Notes: The total time to send and recieve 44.1K samples at the different buffers sizes from CPU->GPU->CPU.
No processing, this is the baseline time to get data back and forth to GPU.
Can see that for most buffer sizes, the limits for 44.1KHz is exceeded! Only at buffer sizes 1-4 is the 44.1KHz rate not successfully met.
The integrated GPU can even do the smaller buffer sizes as It avoids the latency overhead.

## Slide 10: Bidirectional Synthesis Test
Notes: The total time, latency and jitter to send, process and receive 44.1K samples at the different buffers sizes from CPU->GPU->CPU.
This is a complicated physical modelling synthesis method, processing grids with 4096 grid points, 44.1K times a second.
For buffer sizes 1-16, can see the sample rate is not reached.
Higher buffer sizes, above 4096 results in latency and jitter issues.
Sizes 32-256 seem to meet at least the minimum real-time requirements.
Sizes 32-64 and towards 128 meet the recommended requirements.

## Slide 11: General Benchmarks

## Slide 12: GPU Interfacing

## Slide 13: OpenCL
Notes: An open-standard, cross-platform, heterogeneous programming frame-work.
Not limited to GPUs. Great success with CPUs and FPGAs.
Version 1.2 used to support all hardware vendors.

## Slide 14: CUDA
Notes: NVIDIA’s propriety, parallel computing platform for their GPUs.
Driver version / Runtime version: 11.0 / 10.2

## Slide 15: OpenCL Vs CUDA
Bidirectional triangular smoothing test, average time(ms) per buffer.
Notes: Simple triangular smoothing across audio for scaled buffer size. Time is the average time ms to process one buffer of the buffer size.
A simple task, but perfect type of task for GPU.
Run on the two NVIDIA GPUs (CUDA is only supported on NVIDIA)
Solid lines are OpenCL versions.
Dashed lines are CUDA versions.
There is around 0.03ms difference between the OpenCL and NVIDIA versions in favour of the CUDA versions.

## Slide 16: GPU Type

## Slide 17: Discrete GPU
System Memory
CPU
GDDR Memory
GPU
PCIe Bus
Notes: GDDR = Graphics DDR. A synchronous dynamic Random-access memory (SDRAM) designed for GPUs. (Also known as Video RAM (VRAM))
PCIe 3.0 with 16x lanes has a bandwidth of 15.8 GB/s for the NVIDIA 2080 GTI tx
DDR4 2400MHZ has 19.2 GB/s for the CORSAIR DDR4 2400MHz
Data is physically held in memory local to each device. To share data, they must be transferred across the PCIe bus.
PCIe has high bandwidth, but does involve latency.

## Slide 18: Integrated GPU
CPU
GPU
System Memory
Local System Bus
Local System Bus
Notes: In this setup. The system memory is considered unified memory between the two devices.
CPU and GPU can allocate memory and use within their own environment.
Transfers between CPU and GPU is very fast, it all takes place inside the memory, doesn’t need transferring.
Further, there are special techniques like unified memory where a region of memory is allocated to both devices to access. This means both devices can directly access and work with the data in the memory.

## Slide 19: Integrated Vs Discrete
Bidirectional Physical model synthesis test to process 44.1K samples.
Notes: Bidirectional transfers CPU<->GPU physical model synthesis is in OpenCL scaling buffer size. Time is the total time to compute a 44.1K samples.
The solid lines are discrete GPUs.
Dashed line is the integrated GPU.
The integrated GPU starts off faster than most of the GPUs. This is because the latency overhead of moving small buffers back and form CPU<->GPU adds up and although more powerful GPUs, the overhead shadows it.
Around a buffer size of 4. The discrete GPUs surpass the performance of the integrated GPU.
It appears the high end AMD GPU performs the best at most buffer sizes, although the NVIDIA gpus to better at buffer sizes 64 – 512.
AMD might support OpenCL better.

## Slide 20: Memory Types

## Slide 21: Pinned Memory
Pinned Memory
System Memory
GDDR Memory
CPU
GPU
Notes: Or Page-locked memory
Normally, memory is held on each device and to be accessed must be moved to the pinned memory to be transferred to the GPU
Pinned memory, or page-locked memory is a special type of memory that places data ready in pinned memory to be transferred to the GPU straight away.
Changes in memory on one side is reflected on other device.
Good for data needed on both devices. However, suboptimal if the data is only needed on one of the devices.
Limited resource.

## Slide 22: Standard Vs Pinned Memory
Bidirectional Minimal Overhead test, average time(ms) per buffer.
Notes: Test of round-trip data transfer CPU->GPU->CPU for scaled buffer length. Time is average time for one buffer to go back and forth.
OpenCL
Solid lines are the standard memory allocations for 4 discrete GPUs.
Dashed lines are the use of pinned memory for 4 discrete GPUs
Differences between discrete GPUs using standard to pinned memory ranges from 0.04ms to 0.12ms. A significant difference that can add up!
Note the integrated intel GPU does not vary by much? This is because it uses unified memory. Therefore either OpenCL ignores the instruction for pinned memory or it doesn’t make a difference as there are no transfers across buses anyway.

## Slide 23: Comprehensive Results Database
https://muses-dmi.github.io/benchmarking/benchmarking_database_there_and_back_again
harri.renney@uwe.ac.uk
Notes: Test of round-trip data transfer CPU->GPU->CPU for scaled buffer length. Time is average time for one buffer to go back and forth.
OpenCL
Solid lines are the standard memory allocations for 4 discrete GPUs.
Dashed lines are the use of pinned memory for 4 discrete GPUs
Differences between discrete GPUs using standard to pinned memory ranges from 0.04ms to 0.12ms. A significant difference that can add up!
Note the integrated intel GPU does not vary by much? This is because it uses unified memory. Therefore either OpenCL ignores the instruction for pinned memory or it doesn’t make a difference as there are no transfers across buses anyway.

## Slide 24: References
[1] Embedded sound processing with Bela (Oct 26, 2019) YouTube video, Centre for Intelligent Systems[Online]. Available at https://www.youtube.com/watch?v=IfQMC4XGLw4 [27/05/2020].
[2] R. H. Jack, A. Mehrabi, T. Stockman, andA. McPherson. Action-sound latency and theperceived quality of digital musical instruments:Comparing professional percussionists and amateurmusicians.Music Perception: An InterdisciplinaryJournal, 36(1):109–128, 2018
[3] D. Lavry. Sampling theory for digital audio.LavryEngineering, Inc. Available online: http://www.lavryengineering. com/documents/Sampling_Theory.pdf (checked 24.5. 2010), 2004.

## Slide 25: Source Code & Blog
Full write up: https://muses-dmi.github.io/pm_gpus/gpu_accelerated_2d_physical_model
Source code: https://github.com/Harri-Renney/Interactive_2D_Physical_Model